## Slide 1: Common Definition Format
One Data Model Liaison Group
Michael Koster
March 15, 2019

## Slide 2: Common Definition Format
SmartThings Capability Model and Examples
Common Definition Format
UML model
RDF Examples
  ZCL lighting clusters - mapped capabilities
  OCF lighting RTs - mapped capabilities
  ST lighting Capabilities - mapped capabilities
OCF Protocol Binding

## Slide 3: SmartThings Capability Model
Capability Model
Adapt Translate
Adapt Translate
Adapt
Device Models
Device Models
Mesh Devices
Device Models
LAN Devices
C2C Devices
Applications and orchestrations (Groups, Rules, Scenes, Behaviors)
Capability API
Mesh Device API
ST Schema API
LAN/OCF Device API
Instances

## Slide 4: SmartThings Capability Definitions
name: Switch Level
status: live
attributes:
level:
schema:
$ref: IntegerPercent
type: NUMBER
setter: setLevel
commands:
setLevel:
arguments:
- name: level
schema:
type: integer
minimum: 0
maximum: 100
type: NUMBER
required: true
- name: rate
schema:
$ref: PositiveInteger
type: NUMBER
required: false
public: true
id: switchLevel
ocfResourceType: oic.r.light.dimming
version: 1
name: Switch
status: live
attributes:
switch:
schema:
type: object
additionalProperties: false
properties:
value:
$ref: SwitchState
required: ["value"]
type: ENUM
values:
- 'off'
- 'on'
enumCommands:
- command: 'on'
value: 'on'
- command: 'off'
value: 'off'
commands:
'off': arguments: []
'on': arguments: []
public: true
id: switch
ocfResourceType: x.com.st.powerswitch
version: 1

## Slide 5: SmartThings DataType Definitions
title: SwitchState
type: string
enum:
- 'on'
- 'off'
title: IntegerPercent
type: object
additionalProperties: false
properties:
value:
type: integer
minimum: 0
maximum: 100
unit:
type: string
enum: ['%']
default: '%'
required: ["value"]

## Slide 6: Proposal for a Common Definition Format
Common Definition Format
Extract + Map
Extract + Map
Extract + Map
Device Models
Device Models
Device Models
Common Tools and Model Components, Data Types
Models from Various Device Ecosystems

## Slide 7: Supports This Pattern
Abstract Definitions
Events, Actions, Properties
Data Definitions
Feature Extraction
Protocol Binding
ZCL/dotdot Models
XML + XSD
OCF Models
OAS/Swagger

## Slide 8: UML Model
Device Type and Constraints e.g. Thermostat, Light
Composable Capabilities e.g. onoff, level, temperature
Events, Actions, Properties
Data Types, Enums

## Slide 9: Examples
JSON-LD (JSON format with RDF extensions)
Files for semantic definitions of specific types:
  Thing (Device level definitions)
  Capability (onoff, level…)
  InteractionAffordance (Event, Action, Property)
  Data Types (value types, enums)
Definition hierarchy follows the UML model
Core schema for the UML model in JSON-LD
Full examples at: https://github.com/mjkoster/ODM-Examples
(TBD) Thing definitions to apply optionality to Capability sets, Interactions, and Data Types

## Slide 10: ST Sourced definitions
ODM InteractionAffordance definitions, manually extracted from some SmartThings Capability definitions
Attributes map to ODM Property class
Commands map to ODM Action class

## Slide 11: ST Based Capabilities
{
"@id": "st:SwitchCapability",
"rdfs:subClassOf": "odm:Capability",
"rdfs:comment": "Basic On/Off Switch Capability",
"rdfs:label": "SmartThings Switch Capability",
"odm:hasInteractionAffordance": [
"st:Switch.valueProperty",
"st:Switch.onAction",
"st:Switch.offAction"
]
},
{
"@id": "st:SwitchLevelCapability",
"rdfs:subClassOf": "odm:Capability",
"rdfs:comment": "Capability to control the level",
"rdfs:label": "SmartThings SwitchLevel Capability",
"odm:hasInteractionAffordance": [
"st:SwitchLevel.levelProperty",
"st:SwitchLevel.setLevelAction"
]
}

## Slide 12: Properties, Actions, Events
{
"@id": "st:SwitchLevel.levelProperty",
"rdfs:comment": "The current level setting",
"rdfs:label": "SwitchLevel levelProperty",
"@type": "odm.PropertyInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": "st:SwitchLevel.levelData"
},
{
"@id": "st:SwitchLevel.setLevelAction",
"rdfs:comment": "Action to set the level",
"rdfs:label": "SwitchLevel setLevelAction",
"@type": "odm:ActionInteraction",
"rdfs:subClassOf":"odm:InteractionAffordance",
"odm:hasDataItem": [
"st:SwitchLevel.levelData"
"st:SwitchLevel.rateData"
]
}

## Slide 13: Data Items
{
"@id": "st:Switch.valueData",
"rdfs:comment": "value data for Switch (on/off string encoding)",
"rdfs:label": "SmartThings SwitchLevel.levelData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:string",
"js:enum": ["on", "off"]
},
{
"@id": "st:SwitchLevel.levelData",
"rdfs:comment": "Level data for SwitchLevel",
"rdfs:label": "SmartThings SwitchLevel.levelData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 100
},
{
"@id": "st:SwitchLevel.rateData",
"rdfs:comment": "Rate time data for setLevelAction",
"rdfs:label": "SmartThings SwitchLevel.rateData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 65535
}

## Slide 14: ZCL Sourced definitions
ODM InteractionAffordances, manually extracted from ZCL definitions
Attributes map to ODM Property class
Commands map to ODM Action class

## Slide 15: ZCL Example
{
"@id": "zcl:LevelCapability",
"rdfs:subClassOf": "odm:Capability",
"rdfs:comment": "Level Control Capability",
"rdfs:label": "ZCL Level Capability",
"odm:hasInteractionAffordance": [
"zcl.Level.CurrentLevelProperty",
"zcl.Level.RemainingTimeProperty",
"zcl.Level.OnOffTransitionTimeProperty",
"zcl.Level.OnLevelProperty",
"zcl.Level.OnTransitionTimeProperty",
"zcl.Level.OffTransitionTimeProperty",
"zcl.Level.DefaultMoveRateProperty",
"zcl.Level.MoveToLevelAction",
"zcl.Level.MoveAction",
"zcl.Level.StepAction",
"zcl.Level.StopAction",
"zcl.Level.MoveToLevelWithOnOffAction",
"zcl.Level.MoveWithOnOffAction",
"zcl.Level.StepWithOnOffAction"
]
}

## Slide 16: ZCL Example
{
"@id": "zcl.Level.MoveToLevelAction",
"rdfs:comment": "Action move to a given level",
"rdfs:label": "ZCL Level.MoveToLevelAction",
"@type": "odm:ActionInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": [
"zcl:Level.LevelData",
"zcl:Level.TransitionTimeData"
]
},
{
"@id": "zcl.Level.MoveAction",
"rdfs:comment": "Action move at a given rate",
"rdfs:label": "ZCL Level.MoveAction",
"@type": "odm:ActionInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": [
"zcl:Level.MoveModeData",
"zcl:Level.RateData"
]
},

## Slide 17: ZCL Example
{
"@id": "zcl:Level.OffTransitionTimeData",
"rdfs:comment": "Off Transition Time Data",
"rdfs:label": "ZCL Level.OffTransitionTimeData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 65534
},
{
"@id": "zcl:Level.DefaultMoveRateData",
"rdfs:comment": "Default Move Rate Data",
"rdfs:label": "ZCL Level.DefaultMoveRateData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 254
}

## Slide 18: OCF Sourced definitions
ODM InteractionAffordances, manually extracted from OCF Resource Type definitions
Properties map to ODM Property class
Actions added for simple cases like brightness change with ramp time

## Slide 19: OCF Example
{
"@id": "ocf:BrinarySwitchCapability",
"rdfs:subClassOf": "odm:Capability",
"rdfs:comment": "On/Off Switch Capability",
"rdfs:label": "OCF BinarySwitch Capability",
"odm:hasInteractionAffordance": [
"ocf:BinarySwitch.valueProperty",
"ocf.BinarySwitch.OnAction",
"ocf.BInarySwitch.OffAction"
]
},
{
"@id": "ocf:BrightnessCapability",
"rdfs:subClassOf": "odm:Capability",
"rdfs:comment": "Capability to control the brightness",
"rdfs:label": "OCF Brightness Capability",
"odm:hasInteractionAffordance": [
"ocf:Brightness.BrightnessProperty",
"ocf:Brightness.SetBrightnessAction"
]
},

## Slide 20: OCF Example
{
"@id": "ocf:Brightness.brightnessProperty",
"rdfs:comment": "Brightness Property",
"rdfs:label": "OCF Brightness.brightnessProperty",
"@type": "odm.PropertyInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": "ocf:Brightness.brightnessData"
},
{
"@id": "ocf:Brightness.SetBrightnessAction",
"rdfs:comment": "Set Brightness Action",
"rdfs:label": "OCF Brightness.SetBrightnessAction",
"@type": "odm.ActionInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": [
"ocf:Brightness.BrightnessData",
"ocf.RampTime.RampTimeData"
]
},

## Slide 21: OCF Example
{
"@id": "ocf:Brightness.brightnessData",
"rdfs:comment": "Brightness Data",
"rdfs:label": "OCF Brightness.brightnessData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 255
},
{
"@id": "ocf:RampTime.ramptimeData",
"rdfs:comment": "Ramp Time Data",
"rdfs:label": "OCF RampTime.ramptimeData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:integer",
"js:minimum": 0,
"js:maximum": 65535
},

## Slide 22: OCF Example
{
"@id": "ocf:BinarySwitch.OnAction",
"rdfs:comment": "Binary Switch On Action",
"rdfs:label": "OCF BinarySwitch.valueProperty",
"@type": "odm.ActionInteraction",
"rdfs:subClassOf": "odm:InteractionAffordance",
"odm:hasDataItem": "ocf:BinarySwitch.valueOnData"
},
{
"@id": "ocf:BinarySwitch.OnValueData",
"rdfs:comment": "Boolean value for On state",
"rdfs:label": "OCF BinarySwitch.valueData",
"rdfs:subClassOf": "odm:DataItem",
"odm:DataItemType": "js:boolean",
"js:const": true
},

## Slide 23: OCF Protocol Binding/Mapping
Example of an OCF Resource Type definition (OAS/Swagger) file with annotations/extensions for modeling ODM Actions
Mapping can be done to existing OCF types in some cases using CDF annotation
OAS target patterns can be generated using templates and annotated with CDF semantics
Enables an ODM-Capable Bridge or adaptation client to use ODM to generate OCF API calls

## Slide 24: OCF Protocol Binding Example
Thing
Capability
Event/Action/Property
DataItem
Device
Resource Type
Path, Operation
Payload
CDF
OCF
Categories

## Slide 25: OCF Definition with annotations
"title": "Binary Switch",
"version": "v1.1.0-20160519",
"license": {
"name": "copyright 2016-2017 Open Connectivity Foundation, Inc. All rights reserved.",
}
},
"@type": "ocf:BinarySwitchCapability",
"schemes": ["http"],
"consumes": ["application/json"],
"produces": ["application/json"],
"paths": {
"/BinarySwitchResURI" : {
"@type": [
"ocf:BinarySwitch.valueProperty",
"ocf:BinarySwitch.OnAction",
"ocf:BinarySwitch.OffAction"
],

## Slide 26: OCF Definition with annotated paths and operations
"paths": {
"/BinarySwitchResURI" : {
"@type": [
"ocf:BinarySwitch.valueProperty",
"ocf:BinarySwitch.OnAction",
"ocf:BinarySwitch.OffAction"
],
"get": {
"@type": "ocf:BinarySwitch.valueProperty",
}
"post": {
"@type": [
"ocf:BinarySwitch.valueProperty",
"ocf:BinarySwitch.OnAction",
"ocf:BinarySwitch.OffAction"
],
}

## Slide 27: OCF Definition with data annotations
(...)
"minItems": 1,
"readOnly": true,
"type": "array"
},
"value" :
{
"@type": [
"ocf:BinarySwitch.valueData",
"ocf:BinarySwitch.OnValueData",
"ocf:BinarySwitch.OffValueData"
],
"description": "Status of the switch",
"type": "boolean"
},

## Slide 28: Example Device Level Definitoin
{
"@id": "st:DimmableLight",
"rdfs:subClassOf": "odm:Thing",
"rdfs:comment": "Simple Dimmable Light Bulb",
"rdfs:label": "SmartThings DimmableLight",
"odm:hasCapability": [
"st:SwitchCapability",
"st:SwitchLevelCapability"
]
}